## Slide 1
PHYS-204 – Applied Physics
Prof. Neda Adib
Steve Crawford

## Slide 2
PHYS-204
Physics is the driving force,mathematically, that essentially explains how things work within the
universe we live in. Whether it is how fast something accelerates or slows down, how hard or soft impacts another object or surface, to how energy is transferred/released, can all be explained by physics.
Introduction
Through a few very simplistic tests done with some Arduino components, I will attempt to show a few ideas that will use mathematical equations derived from physics to explain the results observed.

## Slide 3
PHYS-204
Experiment Hardware
Below are a few screenshots of the hardware that will be used for the four experiments that will be performed.
The first experiment will observe how a measuring device using sound waves will compare to the speed of sound.
The first experiment will observe how a measuring device using sound waves will compare to the speed of sound.
The second experiment will use the first setup to measure the speed of an object as it is dropped and how gravity is taken into account.
The third experiment will use radians to convert a length measurement, using rotational motion.
The fourth experiment_________________________________________________________

## Slide 4
PHYS-204
To compile the data aquired, along with creating the experiments, I will be utilizing Microsoft Excel and Arduino IDE.

## Slide 5
PHYS-204
Precision of the Ultrasonic Sensor
The first experiment is to determine how accurate the ultrasonic sensor is going to be, along with its speed with that of the approximate speed fo sound, as there are a few factors that affect it. Seeing as how this is a very simplistic experiment, some of those factors will be disregarded.
In this experiment, I ended up changing the object to measure, as my original object was to flexible, and therefore, added an addition variable.
Materials List:
Mega 2560 Board
Ultrasonic sensor HC-SR04
Male to Male Wires
Breadboard
Ruler or tape measurer
Object to act as obstacle

## Slide 6
PHYS-204
Using the Serial Monitor of the Arduino IDE, here you can see the speed of the ultrasonic sensor taking its measurements. This speed, along with the known distance, will then be used to find its accuracy in relation to the Speed of Sound.

## Slide 7
PHYS-204
Trial | Ruler Distance (cm) | Total Roundtrip Distance (m) | Time from Serial Monitor (microseconds) | Roundtrip time (s) | Velocity = distance/time (m/s)
1 | 6 | 0.06 | 309 | 0.000309 | 388.35
2 | 8 | 0.08 | 451 | 0.000451 | 354.77
3 | 10 | 0.1 | 623 | 0.000623 | 321.03
4 | 12 | 0.12 | 732 | 0.000732 | 327.87
5 | 14 | 0.14 | 795 | 0.000795 | 352.20
With now having a couple constants we can now calculate the velocity and round trip time of the ultrasonic sensor. Distances were 6cm, 8cm, 10cm, 12cm, and 14cm in a straight, linear fashion.

## Slide 8
PHYS-204
Data Analysis:
After the experiment was completed for the given lengths, the information was complied and the percentage of error was determined against a constant, or in this case, the speed sound.
Average velocity from table:
348.85m/s
Percent difference:
*343m/s = approx. speed of sound

## Slide 9
PHYS-204
Conclusions:
Discuss the results and comment on the source of errors.
I had found that the angle of the ultrasonic sensor, along with the object of obstruction, if these were not “square” or perpendicular to each other, error was found. I had also found there was a difference in measurement when the height of the sensor was adjusted.
Interestingly, after 8cm, the measurements began to even out in time.
What is the dependence of temperature, humidity and atmospheric pressure on the speed of sound?
Temperature affects Speed of sound by allowing molecules to move slower or faster. Warmer temps, air molecules move faster, therefore allowing sound waves to travel faster. Visa versa for colder temperatures. Humidity affects speed of sound by the density of are molecules. When humidity is low, sound waves travel faster as there is less impedance on the sound wave. The higher humidity, the more of an impact on slowing the speed of sound. Pressure would have no bearing on the speed of sound.

## Slide 10
PHYS-204
Challenges:
This experiment posed the challenge of making sure everything was straight and the object being measured could be left untouched for the sensor to take its measurement. I had to change my original object, as it was unable to stand upright on its own, therefore giving incredible inconsistencies with the experiment.

## Slide 11
PHYS-204
Gravitational Acceleration
Acknowledging the force of gravity on an object’s acceleration will be the focus of this next experiment. Again, seeing as how this is a very simplistic experiment, there will be inaccuracies not accounted for that are external forces acting against the object.

## Slide 12
PHYS-204
This will be the needed components required for this experiment. This experiment will utilize the same components and setup as the previous experiment. The program, however, will be different in the Arduino IDE to utilize gravity acting upon the object.
Materials List:
Mega 2560 Board
Ultrasonic sensor HC-SR04
Male to Male Wires
Breadboard
Object to undergo free fall motion

## Slide 13
PHYS-204
Shown is the Arduino IDE with the appropriate program coding used. This now begins to show the distance of the object from the sensor as it is dropped.

## Slide 14
PHYS-204
Generated from supplied data
Using Microsoft Excel, pasting data into the designated cells, the data is given from the IDE in seconds and measured in centimeters. The spreadsheet converts to meters for the purpose of this experiment.
Unfortunately, the sensor I was using, become unstable, and the experiment data was completely unreliable. Therefore, supplied data was used to finish the experiment.

## Slide 15
PHYS-204
This was from the supplied data given
As seen, the relationship of fall distance vs fall time shows an exponential growth. Which should be expected.

## Slide 16
PHYS-204
Trial | x2 coefficient value from curve fitting | Acceleration (m/s2) = 2* (x2 coefficient)
1 | 4.68 | 9.36 m/s2
2 | 5.02 | 10.08 m/s2
3 | 4.66 | 9.32 m/s2
4 | 4.62 | 9.24 m/s2
5 | 4.73 | 9.46 m/s2
After placing the data into the spreadsheet, x-coeffecient can be gathered and the acceleration in m/s^2 can also be gathered.

## Slide 17
PHYS-204
Data Analysis
Average acceleration from experiment trials:
= 9.49m/s avg
Percentage Difference = 3.2%

## Slide 18
PHYS-204
Conclusion
Discuss the results and comment on the source of errors:
Seeing as how the distance got further away from the point of the object being dropped, the speed had an exponential gain in speed. Sources of error on my part were dropping the object not at a precise time, as well as, the sensor not recognizing the object had moved quick enough.
How much variation is there from trial to trial? What does this indicate about the uncertainty of the result?
From the data provided, the variation had shown only a 3.2% difference in data, however, from my personal experiment, I had over 27% variation, as I could not get the sensor to recognize the the object was dropped quick enough.

## Slide 19
PHYS-204
Challenges:
The main challenge I experienced with this experiment was my sensor becoming unstable, and being unable to complete the experiment with unique data. However, I was able to continue on with the learning concepts of this lab with supplied data. Allowed me to learn the concepts and fundamentals of the lab, however, would have personally valuable to be able to re-create the experiment with unique data.

## Slide 20
PHYS-204
Conservation of Energy
Using the data obtained from the previous experiment, now, will use data to plot and find the difference aspects of conservation of energy. During this lab, Kinetic, Potential, and Total Energy will be evaluated and displayed.

## Slide 21
PHYS-204
The captured data in the chart is displaying calculated results from the time and distance that was created from dropping the object and calculating its Kinetic Energy (K), Potential Energy (U), and the Total Mechanical Energy (E)
Distance is converted from CM to M for this Lab as well.

## Slide 22
PHYS-204
From the captured data placed in the spreadsheet, and the calculated data created from it, the graphs are then plotted. As expected, when kinetic energy increases, potential energy will decrease as at a point, the maximum velocity of the object will be obtained, therefore hitting its energy peak. This point can be observed where kinetic and total energy meet on the graph, thus, showing there is no more potential energy.
The final point on the graph is the eventual stop point of the hitting the ground.

## Slide 23
PHYS-204
DATA VALIDATION:
Final velocity from experimental data (largest velocity): 3.90M/S
Theoretical value of final velocity:
.6510m - .0794m = 0.5716m
=
Percent difference

## Slide 24
PHYS-204
Conclusion:
Discuss the key characteristics of the plot. Consider the times when U is max and min, when K is max and min, and when U and K are the same value. What is the significance of these points?
Key characteristics of the plot are;
Points where Potential Energy and Total Energy are equal, as well as, when Kinetic Energy is equal to total energy.
Another key point, is the equilibrium point, that’s the point where kinetic energy is equal to potential energy. This is the point where energy is at its lowest.
The fact that the plotted points are not straight will also show that there are external acting forces to affect the object during freefall.

## Slide 25
PHYS-204
Conclusion:
What is the trend of the best fit line for the total energy E in your data? If the data is accurate, the total mechanical energy should decrease slightly. Why is that?
The linear fit total energy line has a slight downward, or decrease, graphed. As potential energy is lost, kinetic energy is increased, there is a point where total energy is at its highest, total energy cannot increase beyond this point. It can only be maintained, or abruptly terminated.

## Slide 26
PHYS-204
Rotational Motion
The next experiment will be to use a rotary encoder to measure a linear distance. Being as the encoder has a definitive number of pulses that can be used to measure, this will be taken into account in radians per pulse.

## Slide 27
PHYS-204
Materials List:
Mega 2560 Board
Rotary Encoder Module KY-040
Male to Female Wires
Object to attach onto rotary encoder (e.g. cork, bottle cap, ball)
Ruler or tape measurer
As seen below, the encoder has a lid that has been drilled out to create a pressed-fit onto the encoder. This is allow for the encoder to be held and measure a specified distance to capture the encoder distance in relation to measured distance. This will allow for the percentage of error to be calculated.

## Slide 28
PHYS-204
As seen in the screenshot, the Arduino IDE Serial Monitor is utilized. This was to confirm the encoder was activating as it was rotated.

## Slide 29
PHYS-204
Object diameter: d = 1.746” (44.2cm)
Object radius: r = .873” (22.1cm)
Number of pulses for one revolution: x = 40
Resolution = .1571 rad/pulse
Data Collection
The object that was attached to the encoder, along with the number of pulses per rotation we calculated to find the resolution in Rad/Pulse to define the accuracy of the test.

## Slide 30
PHYS-204
Data Analysis
Trial | Number of pulses N | Encoder distance r N | Measured distance with ruler | Percent difference %
1 | 69 | 239.56 | 26cm | 8.2%
2 | 70 | 243.03 |  | 8.4%
3 | 69 | 239.56 |  | 8.2%
4 | 71 | 246.51 |  | 8.5%
5 | 70 | 243.03 |  | 8.4%
Doing 5 trials, along with the calculations of rads/pulse, this will give the data needed to provide the level of precision with measurement.

## Slide 31
PHYS-204
Conclusions:
Discuss the results and comment on the reasons for errors.
The results were fairly close to each other on each attempt. Some potential flaws I observed was the inability to travel perfectly straight. This will add slight deviations to a linear measurement. Another I saw during my practice runs, was traveling to fast for the encoder to recognize it had rotated.
What are some applications of this measuring technique? Could this measuring system be used to measure surfaces that are not flat?
Some applications would be measuring the length of a field or room. Would also work well for measuring square footage of an area. This could easily used for measuring features or surfaces that are not flat. The measurement would be linear, therefore, that would have to be understood and converted for whatever the application is.

## Slide 32
PHYS-204
Challenges:
The largest challenges with this lab was making sure the object that was attached to the encoder was snug enough to not slip, along with, having a surface that enough friction could be created to actually overcome the tension inside the encoder.
Another challenge was making sure to run the encoder in a straight line with no deviations so as to have as straight a line as possible.

## Slide 33
PHYS-204
HALL EFFECT EXPERIMENT
This last experiment was to test how a Hall Effect sensor works in relation to a magnet entering into the region of the sensor.

## Slide 34
PHYS-204
Materials List:
ESP32 microprocessor
Micro-USB cable
Magnet
This is the materials list, along with a microprocessor hooked and running. I also happened to use a breadboard in this instance, as I wanted the board a bit more secure while attempting the experiment, however, it is was not necessary.

## Slide 35
PHYS-204
As in all the experiments used within this presentation, the Arduino IDE was utilized in the coding of the board.

## Slide 36
PHYS-204
Once the magnet was brought within a range of the Hall sensor, and then flipped over and repeated, that data was then inserted into a spreadsheet to create a line chart to show what happens with first the south end of the magnet was brought into range of the sensor, then the north end was brought into range.

## Slide 37
PHYS-204
Conclusion:
Discuss the results and comment on how the Hall sensor works.
  When the magnet was brought into close range of the sensor, the sensor began recording a negative measurement. When the magnet was flipped over, and the same process repeated, a positive measurement was recorded. While the magnet was not near the sensor, a measurement of zero was recorded. The Sensor works by detecting the magnetic flux density within its area. Once the density is beyond the pre-determined threshold, it begins generating a voltage signal in relation to the flux density and polarity.
What are some applications for the Hall effect sensor?
  Hall effect sensors are used in extensively in the automotive world for ignition timing, in machine controls for motor location, in dishwashers for the spray arm to acknowledge its movement. Essentially, anything that has a rotational movement that will need to either acknowledged or recorded, will more than likely contain a hall effect sensor

## Slide 38
PHYS-204
Challenges:
The challenge that was ran into was moving the magnet either too slow or too quickly toward or away from the Hall sensor to obtain data that was not obscured. Moving too quickly provided very quick spikes in data, and too slowly the data was elongated. Finding a consistent speed was difficult to repeat for both sides of the magnet.

## Slide 39
PHYS-204
Career Skills:
After working on these experiments, learning the mathematical formulas, and physically applying them to an application, the skills gained would be helpful within many careers.
To name a few skills obtained:
Understanding of how to convert radians to liner distance
Using time to calculate distance with a known speed constant
Plotting points and creating a line chart to display data
Calculating data and recognizing potential errors in a setup or experiment
Becoming proficient with Arduino IDE for programming and testing

## Slide 40
PHYS-204
Project Conclusions
Applied Physics has given me a heightened level of understanding of how the world actually works. Before the understanding of the mathematical formulas learned within this course, along with the experiments within the lab, a rudimentary understanding was what was understood about the aspects that govern everyday workings.
Understanding how friction works in relation to energy needed to move an object, or how electricity flows, or how magnetic fields affect each other, all of this has heightened my level of understanding.